## Slide 1: Class Experiment
Data and Terminology

## Slide 2: Timing Terminology

## Slide 3: Our Experiment: One Session
Session: One set of functional and anatomical scans
e.g., In patients, may have one session before treatment and one after

## Slide 4: Protocol File
Brain Voyager file type: .prt (protocol)
Text file (can be edited by a text editor

## Slide 5: Protocol File
…
GUI view
Text Editor view

## Slide 6: Protocol Terminology
  bodies
  faces
  hands
  scrambled
  black = baseline fixation
1 run
Run: Continuous collection of data over time
typically 3-10 minutes
Condition: type of stimuli or task
5 conditions (or 4 conditions
+ baseline)
Some terminology varies between labs
e.g., “scan” can mean run, volume or session

## Slide 7: Protocol Terminology
  bodies
  faces
  hands
  scrambled
  black = baseline fixation
1st epoch
or block of faces
Epoch: One block of trials for a condition
Block Design: Experiment in which trials are grouped into blocks
-- typically ~15 s/block (range 10-30)

## Slide 8: Protocol
1st face epoch
TIME
800-ms
stimulus
duration (SD)
200-ms
intertrial interval (ITI)
1-s stimulus onset asynchrony (SOA)
Note for cognitive science sticklers: Because stimuli are unmasked and visual processing likely continues in iconic memory during the ITI (and because the HRF isn’t that great temporally anyway), our models will assume visual activation is high throughout the epoch and does not fluctuate between SD and ITI
Trial 1
Trial 2
RUN
TRIALS

## Slide 9: Protocol Terminology
1st trial
of faces left

## Slide 10: What happens at the scanner in a session?

## Slide 11: fMRI Experiment Stages
1) Prepare subject
  Consent form
  Safety screening
  Instructions and practice trials if appropriate

## Slide 12: fMRI Experiment Stages
2) Sagittal scout images
Take images along the midline to plan slices
Note: That’s one g, two t’s
In this example, these are the functional slices we want: 52 slices x 2.5 mm

## Slide 13: fMRI Experiment Stages
3) Shimming
  putting body in magnetic field makes it non-uniform
  adjust 3 orthogonal weak magnets to make magnetic field as homogenous as possible in functionally scanned volume

## Slide 14: fMRI Experiment Stages
4) Take anatomical (T1) images
  high-resolution images (e.g., 1-mm resolution)
  3D data: 3 spatial dimensions, sampled at one point in time
1 slice (sagittal)
2D
Anonymous
[defaced]

## Slide 15: Zooming In
1 mm
1 mm
1 mm

## Slide 16: Anatomical (T1) Scan
Brain Voyager file type: .amr (anatomical MR)
3D (stack of 2D slices)
Our data: 176 slices at 1-mm isotropic resolution

## Slide 17: One Volume
x
+
-
z
-
+
+
-
y
L
R
Volume = One stacked set of slices that forms a full 3D sample of the desired brain volume
Brain Voyager file type: .vmr (volumetric MR)
3D
Our data: 176 slices at 1-mm isotropic resolution

## Slide 18: Left is what?!!!
Neurologic (i.e. sensible) convention
  left is left, right is right
L
R
Radiologic (i.e. stupid) convention
  left is right, right is left
R
L
Note: Make sure you know what your magnet and software are doing before publishing left/right info!
x = 0
-
+
x = 0
+
-

## Slide 19: Pro Tip
Put a vitamin E capsule on the one side (always the same side!) of the subject’s head or coil.

## Slide 20: fMRI Experiment Stages
5) Take functional (T2*) images
  medium-resolution images (e.g., 2.5-mm resolution)
  4D data: 3 spatial dimensions x time dimension

## Slide 21: Functional Activation Changes Over Time
Source: Kwong et al., 1992
Flickering Checkerboard
OFF (60 s) - ON (60 s) - OFF (60 s) - ON (60 s)

## Slide 22: Functional Volume
Volume: One stacked set of slices that forms a full sample of the desired brain volume
Brain Voyager file type: .fmr (functional MR)
appears 3D (stack) but you can see 4th dimension (time) through movie
Our data: 52 slices at 2.5-mm isotropic resolution and 1-s temporal resolution

## Slide 23: Volumes in Time
… 340 volumes
We collected one volume every second for 340 s
One can think of volumes as spatial (3D units) or temporal (e.g, 1 volume = 1 s)
340 volumes

## Slide 24: Slice Terminology
SLICE THICKNESS
e.g., 2.5 mm
IN-PLANE SLICE
Field of View (FOV)
e.g., 21.0 cm
VOXEL
(Volumetric Pixel)
In-plane resolution
e.g., 210 mm / 84
= 2.5 mm
2.5 mm
2.5 mm
2.5 mm

## Slide 25: Voxel Size
EXCEPT when the activated region does not fill the voxel (partial voluming)
3 x 3 x 6
= 54 mm3
e.g., SNR = 100
3 x 3 x 3
= 27 mm3
e.g., SNR = 71
2.1 x 2.1 x 6
= 27 mm3
e.g., SNR = 71
isotropic
same size in 3 directions
non-isotropic
non-isotropic
In general, larger voxels buy you more SNR.

## Slide 26: Explain voxel sizes clearly … especially if Jody will be your thesis examiner!
Anatomical voxel sizes are typically 1-mm isotropic
Functional voxel sizes are typically 2- to 3-mm isotropic
Software may resample functional voxel sizes
  e.g., Brain Voyager resamples functional voxels to 1-, 2- or 3-mm isovoxel resolution
Thus a statement like, ”[Region X] comprised Y voxels” is unclear.
Pop quiz: Which of the following is correct for describing 3-mm isovoxel resolution?
    Functional voxels were 3 mm3.
    Functional voxels were (3 mm)3.
    A or B. They’re equivalent.

## Slide 27: Volumetric Functional
Brain Voyager file type: .vtc (volumetric time course)
appears 3D (stack) but you has 4th dimension (time)
We can render the functional data in the same volumetric coordinate system as the anatomical
This shows the first functional volume of the first localizer

## Slide 28: Thinking About Functional Data
Raw data
one run of our localizer
  52 slices x 84 x 84
    366,912 voxels
  2.5-mm isovoxel resolution
  340 volumes (time points) @ TR=1  5 min: 40 s/run
  52 x 84 x 84 x 340 = 124M data points (value = signal intensity)
Processed data
4 dimensions
  3 spatial dimensions
    x, y, z
  1 time dimension
One way to think about it
  340 volumes
Another way to think about it
  366,912 time courses
Functional data resampled to Native VTC with (2 mm)3 resolution and masked to exclude voxels outside the brain
  194,003 functional voxels x 340 time points
from Brain Voyager Documentation
t1
t2
t3
t4
t340
…

## Slide 29: Resampling and Masking
Resampled data (vtc)
resample data to (2 mm)3 resolution
exclude voxels outside the brain
 194,003 functional voxels x 340 time points
t1
t2
t3
t4
t340
…
Raw data (fmr)
one run of our localizer
  52 slices x 84 x 84
    366,912 voxels of (2.5 mm)3

## Slide 30: Which ”voxel size”?
Native anatomical (slices)
  1 mm isotropic
Native functional (slices)
  2.5 mm isotropic
Resampled anatomical (volumetric vmr)
  1 mm isotropic
Resampled anatomical (volumetric vtc)
  2 mm isotropic
this is what matters most for data quality
should be <= native resolution (but making this really small gives you huge files that take a long time to process)
native = resolution collected from the scanner (unresampled)

## Slide 31: Resampling
Data may have to be resampled
  to go from slices to volumes
    e.g., BrainVoyager offers vtc resolutions of (1 mm)3, (2 mm)3 or (3 mm) 3
  to get all participants in the same spatial coordinate system so you can do group stats
  when correcting for head motion
  when doing different filtering (e.g., spatial smoothing)
Example
resampling from 2.5-mm .fmr to create 2-mm .vtc
white = 1 mm cubes for reference
green = 2.5 mm native func
red = 2 mm resampled func
e.g., highlighted red voxel can be derived from weighted combination of green voxels: (1 x lower left + 3 x lower right)/4

## Slide 32: MRI vs. fMRI
MRI
fMRI
One 3D volume
series of 3D volumes (i.e., 4D data)
(e.g., every 2 sec for 5 mins)
high resolution
(1 mm)
low resolution
(~2.5-3 mm)
…
Notes: I is for Imaging
Imaging parameters are different MRI ”Anatomicals” aim to maximize tissue contrast
fMRI to maximize functional contrast.

## Slide 33: Spot the Differences

## Slide 34: T1, T2 and T2*
T1 = “tee one” = anatomical scan, normal contrast (GM darker than WM), typical anatomical for cogneuro expts
T2 = “tee two” = anatomical scan, reverse contrast (GM brighter than WM), used in clinical scan and animal scans because sometimes it can give better contrast between tissues (e.g., tumor vs. normal tissue, GM vs. WM), susceptibility artifacts
T2* = “tee two star” = functional scan (usually EPI), reverse contrast (GM brighter than WM), susceptibility artifacts, sensitive to BOLD (which is a fine-scale susceptibility artifact)
tumor in T1 vs. T2
normal brain in T1 vs. T2
normal brain in T2*, showing susceptibility artifacts

## Slide 35: Data Organization
Anatomical or functional data files are basically just matrices of intensity values
Matrices may be 2D for single slices or 3D for one volume or 4D for series of volumes
Image from Poldrack et al., 2011

## Slide 36: Header Information
Headers
  contain info about scanning parameters in structured format
  may be separate from data (e.g., SPM/Analyze uses separate .hdr and .img files) or combined with data (e.g., BV .vmr file includes both header and data)

## Slide 37: Working With Data
Different scanners and packages use different formats
Examples
  Siemens: DICOM format (Digital Imaging and Communications in Medicine)
  SPM: Analyze
  MNI: MINC
  Brain Voyager: vmr, vtc, etc.
NIfTI (Neuroimaging Informatics Technology Initiative)
  the new default for file formats
  commonly used format useful for transferring data between software packages
  other variants (e.g., GIfTI for surfaces)
Can often hack files (esp. text-only files) faster than modifying via GUIs

## Slide 38: BIDS = Brain Imaging Data Structure

## Slide 39: BIDS

## Slide 40: Dummy scans or Disdaqs
Discarded data acquisitions: trashed volumes at the beginning of a run before the magnet has reached a steady state
The scanner may throw out the disdaqs before it saves the data or it may save them too, in which case you have to discard them in your software
Sometimes it can take awhile for the subject to reach a steady state too -- Startle response!

## Slide 41: Dummy Scans
Two options for dealing with dummy scans
Discard them at the scanner
Discard them in your analysis software
Example, for our localizer protocol we want 340 real (non-discarded) volumes (TR = 1 s). Say we decided to add 5 dummy scans.
Tell the MR technician to collect 345 volumes, count the first 5 as dummy scans and save only the last 340. In your software, do not skip any volumes.
Tell the MR technician to collect 345 volumes and save all of them. Tell your analysis software to skip the first 5.

## Slide 42: Synchronizing your data collection and your stimulus/task software
All of our stats depend on modelling when things happened. If your model is misaligned with the data, say by 5 s in the previous example, your estimates of activation will be incorrect.

## Slide 43: Protocol
If this is your protocol, you want to be sure that the first body was presented 16 s in (not 11 s or 21 s if you don’t properly account for the 5 s of dummy scans)

## Slide 44: Timing Strategies at CFMM
The scanner console emits one “trigger” at the start of each volume (i.e., first slice), starting with the “real” (non-dummy) volumes (i.e., no trigger is sent for dummy volumes)
There is a trigger box that can plug into the USB port of your stimulus computer/laptop
The trigger is read in as the equivalent to the letter “T” (letter configuration) or the number “5” (number configuration, where 5 is the number above the T key but not 5 on the number pad)
The stimulus computer can count triggers to know when to present stimuli
e.g., presenting body #1 at the start of the 17th real volume (i.e., after 16 s), body #2 on the 18th real volume (i.e., after 17 s) and so on
You can also allow your software to be free running (e.g., present body #1 16 s after the program starts)
This is fine if both the stimulus computer and the scanner console have accurate timing but some people prefer to use triggers
Trigger timing is one of the things most likely to go wrong in an fMRI session so pilot test this carefully (in pilot time, when you’re not paying $150/h and you don’t have a participant getting bored in the scanner)