## Slide 1: fMRI Analysis with emphasis on the General Linear Model
http://www.fmri4newbies.com/
Jody Culham
Brain and Mind Institute
Department of Psychology
Western University
Last Update: September 24, 2020
Last Course: Psychology 9223, F2020, Western University

## Slide 2: Course Approach
Minimal math; intuitions
Start with one voxel in one run of one participant two conditions
  correlation
  GLM
Enhance understanding of GLM
  Extend to multiple conditions
  Extend to multiple runs
  Consider corrections for violations of assumptions
  Learn how preprocessing is beneficial
  Extend to multiple participants
  Extend to more complex situations (event-related deconvolution, parametric models, ANOVAs)

## Slide 3: The GLM for Math Whizzes
Friston 2005, Ann. Rev. Psych.

## Slide 4: A Simple Correlation

## Slide 5: Visual Cortex (V1)
To begin, let’s examine one functional voxel in visual cortex
Visual cortex is at the back of the cerebral cortex, in the occipital lobe, with primary visual cortex (V1) falling in Brodman Area 17 (blue in left image below)
V1 and other visual areas are organized into a map of the visual field,
  the centre (where our participant is fixating) at the pole and more periphearl locations represented farther forward
Because our stimuli were relatively small and near fixation, we expect parafoveal activation
Occipital Pole represents parafoveal vision (near fixation point) for early visual areas, V1/V2/V3

## Slide 6: The simplest case: 1 voxel, 2 states
What would be the expected time course for a brain area (e.g., V1) that responded to visual stimulation?
Early visual cortex
Visual stimulation

## Slide 7: Expected Neural Activity
Because we don’t know what units the y-axis is in, nor how big the effect will be, we can arbitrarily scale the predictor from 0 to 1

## Slide 8: BOLD Time Course Blood Oxygenation Level-Dependent Signal
Positive BOLD response
Initial Dip
Overshoot
Post-stimulus Undershoot
0
1
2
3
BOLD Response (% signal change)
Time
Stimulus

## Slide 9: Modelling the HRF: Two-gamma function

## Slide 10: Incorporating the HRF
Neural activity
Neurovascular coupling
Signal measured in fMRI
=
Model of neural activity
Model of HRF
Model of expected BOLD signal
convolution

## Slide 11: Predicted vs. Actual Time Course
Predicted BOLD response
Actual BOLD response in Voxel A

## Slide 12: Pearson Correlation
r = .8
r2 = .64

## Slide 13: Y-Axis Converted to %BSC
% BOLD Signal Change (%BSC) for each time point
Y%BSC = (Yraw – Ybaseline)/Ybaseline)*100
Activation
(Raw Signal)
Time (1-s volumes)
Remember this is the change in BOLD, not neural activation
  Block designs:
  Big: several %
  Moderate: 1%
  Small: fraction of 1%
Activation
(% Signal Change)

## Slide 14: Alternative to %BSC
z-score
  Yz = (Yraw – Ymean)/YSD over time)
  units become SDs
  Ymean and YSD are specific to a run
  works fine if all conditions are within one run
  bad idea if different conditions are in different runs because different runs will have different SDs (due to potenitally different effect sizes and potentially different noise levels)

## Slide 15: Units don’t affect r

## Slide 16: Which time course shows the clearest evidence of a visual stimulation effect? Which shows the least?

## Slide 17
1% BSC effect
2% BSC effect
low noise
med noise
high noise
r2 = .34
slope = 0.97
r2 =.11
slope = 0.97
r2 = .90
slope = 2.04
r2 = .68
slope = 1.97
r2 = .35
slope = 1.97
r2 = .71
slope = 1.04

## Slide 18: Understanding correlations
How big is the activation difference?
  slope = activation difference between the two conditions
  1% BSC or 2% BSC
How big is the activation difference, taking into account how noisy the data is?
  σ = variance
  r2
    = σexplained/ σtotal
    = σexplained/ (σexplained+ σunexplained)
How likely is it that an activation difference of this size could occur due to chance?
  consider r2 in light of how much data we have (df = degrees of freedom)

## Slide 19: fMRI Statistics
The noisiness of the data can be derived from two possible sources
First level
  variability over time
Second level
  variability over participants
Because we only have one run from one participant, we can only do the former
When we discuss group data, we will learn how to do the latter

## Slide 20: Which data is more trustworthy?

## Slide 21: Degrees of Freedom
Total degrees of freedom = 340 data points (volumes)
Model degrees of freedom
  For a correlation, there are 2 df (slope + intercept)
Residual degrees of freedom
  Total – model
  340 – 2 = 338

## Slide 22: Statistical Errors
Is there a real activation difference in a given voxel?
No
Yes
Does the statistical test indicate an activation difference in the given voxel?
Type I Error
(false positive)
Correct
decision
(true positive)
Correct
decision
(correct
rejection)
No
Yes
Type II Error
(incorrect
rejection)
Limit ⍺ to p < .05
(5%)

## Slide 23: Statistical significance
alpha = .05 (two-tailed)
df = 338
rcritical = .106
|r| > .106 is statistically significant
https://mathcracker.com/critical-correlation-calculator#results

## Slide 24: Voxelwise statistical tests Just a few more times…
BV resampled the functional data into standard (MNI) space at a resolution of 2 x 2 x 2 mm
We discarded voxels outside the brain in the volumetric functional (vtc) file
This led to 194,003 functional voxels
So we just have to do this 194,003 more times…

## Slide 25
Voxel A
r = .796
Voxel B
r = .358
Voxel C
r = .457
Voxel D
r = -.374
A
C
B
D
Visual Stimulation Predictor
x = 108

## Slide 26
r >= .11
(max r = 1)
voxelwise p < .05
Minimum (Threshold)
Maximum
Minimum (Threshold)
Maximum
Positive Correlations
(Visual Stimuli > Baseline)
Negative Correlations
(Visual Stimuli < Baseline)
g
Legitimate activation expected in gray matter clusters
Generally NO legitimate activation expected in
ventricles
outside head
in white matter unless experiments are done carefully (Gawryluk, Mazerolle & D’Arcy, 2014)
single voxels unless you’re in fine nuclei
Sniff test failed!

## Slide 27
r >= .29
(max r >= 1)
voxelwise p < .00000026
[familywise (Bonferroni) p < .05]
r > 0
(max r >= 1)
voxelwise p = 1
r >= .11
(max r > 1)
voxelwise p < .05
r >= .6
(max r >= 1)
voxelwise p < 10-34
Effect of Changing Minimum (Threshold)
Minimum (Threshold)
Maximum
Minimum (Threshold)
Maximum
Positive Correlations
(Visual Stimuli > Baseline)
Negative Correlations
(Visual Stimuli < Baseline)
c
superimposed on functional vs. anatomical scan

## Slide 28
r > 0
(max r >= 1)
voxelwise p = 1
r > 0
(max r >= .5)
voxelwise p = 1
Effect of Changing Maximum
c
r > 0
(max r >= .8)
voxelwise p = 1
Minimum (Threshold)
Maximum
Minimum (Threshold)
Maximum
Positive Correlations
(Visual Stimuli > Baseline)
Negative Correlations
(Visual Stimuli < Baseline)
Recommendation:
Set maximum around the most significant voxel so that look-up table spans the full range