## Slide 1: Preprocessing

## Slide 2: Example: GLM with 4 predictors
fMRI Signal
=
Residuals
Design Matrix
+
“what we CAN explain”
“what we CANNOT explain”
=
+
Betas
x
“how much of it we CAN explain”
“our data”
=
+
x
Statistical significance is basically a ratio of explained to unexplained variance
x Faces
x Hands
x Bodies
x Scram
+
+
+

## Slide 3: So how can we improve our statistics?
Increase signal
  slice scan time correction
  spatial smoothing
Decrease residuals (noise)
  spatial smoothing
  motion correction
  high-pass temporal filtering
Moving variance from unexplained (noise) to explained
  predictors of no interest
    motion parameters
    signals from noisy areas (e.g., white matter)

## Slide 4: Two Stages
Preprocessing of data before running GLM
Include PONIs in GLM

## Slide 5: fMR Preprocessing

## Slide 6: VTC Preprocessing

## Slide 7: Increasing Signal
Slice Scan-time Correction

## Slide 8: Slice Order
Non-
Interleaved;
Descending
Problem with non-interleaved slices:
excitation of one slice may carry over to next slice
If TR = 2, the first slice is collected almost a full TR (e.g., 2 s) before the last slice

## Slide 9: Slice Order
Interleaved;
Descending
If TR = 2, the first yellow slice is collected almost a full TR (e.g., 2 s) before the last pink slice

## Slide 10: Slice Order
Multiband Imaging
Collects multiple slices simultaneously
e.g., multiband 4 collects 4 slices at a time
allows you to sample the whole brain in a short TR
If TR = 1, the red slices are collected almost a full TR (e.g., 1 s) before the purple slices

## Slide 11: Slice Scan Time Correction

## Slide 12: Slice Scan Time Correction
Source: Brain Voyager documentation
interpolates the data from each slice such that is is as if each slice had been acquired at the same time

## Slide 13: SSTC: Not So Clear Cut
SSTC interacts with motion correction
  Interpolation  motion affects multiple volumes instead of just one
Now that functional data is collected more rapidly (due to multiband imaging… stay tuned), we can collect whole-brain volumes with TR = 1 s
  Nevertheless, BrainVoyager recommends applying SSTC

## Slide 14: Increasing Signal; Decreasing Noise
Spatial Smoothing

## Slide 15: 3D (No interpolation)

## Slide 16: 2D (No interpolation)

## Slide 17: 1D (No interpolation)

## Slide 18: 1D (No interpolation)
0 | 0 | 0 | 53 | 53 | 53 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 127 | 127 | 127 | 139 | 139 | 139 | 123 | 123 | 123
3-mm functional voxels shown at 1-mm resolution

## Slide 19: Spatial Smoothing
Gaussian kernel
smooth each voxel by a Gaussian or normal function, such that the nearest neighboring voxels have the strongest weighting
Maximum
Half-Maximum
Full Width at Half-Maximum
(FWHM)
FWHM = 6
0
1
2
3
4
5
6
7
8
-8
-7
-6
-5
-4
-3
-2
-1

## Slide 20: Gaussian Smoothing (4-mm) FWHM on One Voxel
0 | 0 | 0 | 53 | 53 | 53 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 127 | 127 | 127 | 139 | 139 | 139 | 123 | 123 | 123
Smoothed V14 ~= 0.1xV11 + 0.3xV12 + 0.75xV13 + 1xV14 + 0.75xV15 + 0.3xV16 + 0.1xV17
0.1 + 0.3 + 0.75 + 1 + 0.75 + 0.3 + 0.1

## Slide 21: Repeat for every voxel…
0 | 0 | 0 | 53 | 53 | 53 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 127 | 127 | 127 | 139 | 139 | 139 | 123 | 123 | 123

## Slide 22: Effect of Smoothing
pre-smoothing
post-smooothing (4-mm FWHM)

## Slide 23: Gaussian Smoothing (8-mm) FWHM on One Voxel
0 | 0 | 0 | 53 | 53 | 53 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 155 | 155 | 155 | 164 | 164 | 164 | 128 | 128 | 128 | 127 | 127 | 127 | 139 | 139 | 139 | 123 | 123 | 123
Now voxels within +/- 8 mm have an effect

## Slide 24: Why Smooth?
Signal
Smoothed Signal
Noise
Smoothed Noise
(Signal + Noise)
Smoothed (Signal + Noise)
outside
brain
gray
matter
white
matter
gray
matter
outside
brain
Signal sums
Random noise cancels

## Slide 25: 1D - 2D – 3D Gaussians

## Slide 26: Effects of Spatial Smoothing on Activity
No smoothing
4-mm FWHM
7-mm FWHM
10-mm FWHM
Notes: LO Localizer, 1 run, mt.10_06_03_10_MAG_THPGLMF2c_SD3DSSXXXXXmm.fmr, Intact > Scrambled, t>3.5

## Slide 27: Should you spatially smooth?
Advantages
  Increases Signal to Noise Ratio (SNR)
    Matched Filter Theorem: Maximum increase in SNR by filter with same shape/size as signal
  Reduces number of comparisons
    Allows application of Gaussian Field Theory
  May improve comparisons across subjects
    Signal may be spread widely across cortex, due to intersubject variability
Disadvantages
  Reduces spatial resolution
  Challenging to smooth accurately if size/shape of signal is not known
Slide from Duke course
“Why would you spend $4 million to buy an MRI scanner and then blur the data till it looked like PET?”
-- Ravi Menon

## Slide 28: Decreasing Noise
Temporal Filtering

## Slide 29: BV Preprocessing Options

## Slide 30: Components of Time Course Data
Source: Smith chapter in Functional MRI: An Introduction to Methods

## Slide 31: Fourier Analysis
Any waveform (like a time series) can be composed into a series of sine waves (each with a frequency and an amplitude). These sine waves can be plotted with amplitude as a function of frequency.

## Slide 32: Fourier Spectrum for Data at Rest
Even in a “resting state scan” (i.e., when subject isn’t doing a task), certain frequencies are present
Respiration
every 4-10 sec (0.3 Hz)
moving chest distorts susceptibility
Cardiac Cycle
every ~1 sec (0.9 Hz)
pulsing motion, blood changes
Solutions
gating
avoiding paradigms at those frequencies

## Slide 33: “Low-Pass” vs. “High-Pass”
Low-pass
pass the low frequencies through the filter
remove the high frequencies
you could also call this temporal smoothing
High-pass
pass the high frequencies through the filter
remove the low frequencies

## Slide 34: Temporal Filtering You Should Usually Do: LTR + High-Pass
Frequency (Hz)
Power
Frequency (Hz)
Power
Frequency (Hz)
Power
Raw
LTR
(linear trend removal)
LTR
+
THP3c
(temporal high-pass 3 cycles/run)

## Slide 35: Temporal Filtering You Should Usually Do: LTR + High-Pass
Frequency (Hz)
Power
Raw

## Slide 36: Temporal Filtering You Should Usually Do: LTR + High-Pass
Frequency (Hz)
Power
Frequency (Hz)
Power
Raw
LTR
(linear trend removal)

## Slide 37: Temporal Filtering You Should Usually Do: LTR + High-Pass
Frequency (Hz)
Power
Frequency (Hz)
Power
Raw
LTR
(linear trend removal)
there’s still low-frequency noise in the signal
e.g., frequencies below 3 cycles/run
  … like 2 cycles/run
  … or 1 cycle/run
  … and other frequencies
we can remove these low frequencies from the signal
we want to stop the low frequencies from passing through our filter but let the high frequencies pass
  ∴ the filter we use is called a high-pass filter
  cutoff = 0.009 Hz
3 cycles/run
= 3 cycles/340 s
= 0.009 cycles/s
= 0.009 Hz
Pass
Block

## Slide 38: Temporal Filtering You Should Usually Do: LTR + High-Pass
Frequency (Hz)
Power
Frequency (Hz)
Power
Frequency (Hz)
Power
Raw
LTR
(linear trend removal)
LTR
+
THP3c
(temporal high-pass 3 cycles/run)
Pass
Block
Pass
Block

## Slide 39: Temporal Filtering You Should Not Do: Aggressive High-Pass
Raw
LTR
+
THP3c
(temporal high-pass 3 cycles/run
= .009 Hz)
LTR
+
THP24c
(temporal high-pass 24 cycles/run
= ? Hz)
Frequency (Hz)
Power
Frequency (Hz)
Power
Pass
Block
Frequency (Hz)
Power
Pass
Block
WTF Happened?!

## Slide 40: Low-Pass Filtering: Looks great but causes violations of statistical assumptions regarding autocorrelation
LTR
+
THP3c
(temporal high-pass 3 cycles/run)
+
TDTS2.8s
(Time-domain temporal smoothing
Gaussian FWHM 2.8 s)
LTR
+
THP3c
(temporal high-pass 3 cycles/run
= .009 Hz)
Frequency (Hz)
Power
Pass
Block
Frequency (Hz)
Power
Pass
Block
Temporal smoothing reduces high-frequency power

## Slide 41: Moving Variance from Noise to Signal
Predictors of No Interest

## Slide 42: Predictors of No Interest
Often there is variance that is known but not particularly interesting
We can create predictors that account for this variance and thus remove it from the residuals
Common examples
  regressors for experimental components
    motor responses
    instruction periods
    error trials
  regressors for known sources of noise
    motion
    respiratory/cardiac signals
    unknown noise

## Slide 43: PONIs are not a panacea
noise sources do not always match their measurements
  e.g., motion can lead to transient effects
  can include derivatives
PONIs utilize degrees of freedom and including too many reduces statistical power
If PONIs are correlated with predictors of interest (POIs), they can reduce the significance of the POIs
  common problem with motion predictors
  common problem with events that must occur in a particular order (e.g. delay paradigms)

## Slide 44: Order of Preprocessing Steps is Important
Thought question: Why should you run motion correction before temporal preprocessing (e.g., linear trend removal)?
If you execute all the steps together, software like Brain Voyager will execute the steps in the appropriate order
Be careful if you decide to manually run the steps sequentially. Some steps should be done before others.

## Slide 45: SSTC and 3DMC Interact

## Slide 46: Take-Home Messages
Look at your data
Work with your physicist to minimize physical noise
Design your experiments to minimize physiological noise
Motion is the worst problem: When in doubt, throw it out
Preprocessing is not always a “one size fits all” exercise