## Slide 1: Group Analyses
1. Get all the subjects’ brains into a common space
  Talairach space
  MNI space
  cortex-based alignment
2A. Do group statistics
  Random Effects GLM
and/or
2B. Use a Region of Interest Approach

## Slide 2: Voxelwise Group Analyses
Fixed vs. Random Effects

## Slide 3
Caveat: I wasn’t able to get all the course data in time to update these slides so they use different data set
This other data set has conditions with faces and objects
In the tutorial, you will work with the course dataset

## Slide 4: Example
Three subjects
Three conditions: Baseline, Faces, Objects
For simplicity, just consider one voxel in FFA

## Slide 5: Stupid Way: Concatenated Fixed Effects (FFX)
Concatenate data, pretend you have one subject who did three runs
(Pay attention to the black line; ignore colored lines)

## Slide 6: Stupid Way: Concatenated Fixed Effects (FFX)
Make one predictor for Faces and one for Objects (2 df)
Scale predictors (by beta weights)
Note why this is stupid
  Assumes all subject show same magnitude of activation
  Errors in this assumption   residuals

## Slide 7: Better Way: Separate Subjects FFX (SPSB in BV)
Don’t concatenate
Separate predictors for 3 subjects x 2 conditions
  6 df

## Slide 8: Problem: Separate Subjects FFX
We could do business-as-usual GLM and see if predictors account for significant variance considering noise
Effectively, we are asking how confident we are that this effect is true (not due to chance) in these three subjects (and only these three subjects)
BUT usually, we want to generalize to the population from which we sampled

## Slide 9: Best Way: Random Effects (RFX)

## Slide 10: Second-level analysis
Nothing too complicated… it’s effectively just a paired-samples t test
A paired-samples t test is the same as a one-sample t test on differences
Subject | βFaces | βObjects | Difference βFaces - βObjects
S1 | 0.552 | 0.105 | 0.447
S2 | 2.061 | 1.121 | 0.940
S3 | 1.019 | 0.247 | 0.772
Mean |  |  | 0.719
SD |  |  | 0.250
SEM [=SD/sqrt(N)] |  |  | 0.145
tcrit(df=3) |  |  | 4.3
95%CI lower (= mean – (t*SEM)) |  |  | 0.097
95%CI lower (= mean + (t*SEM)) |  |  | 1.34
Estimated Distribution
of Differences
does not include zero
 significant (p<.05)
0.719
0.097
1.34
95% CI
0
Oops, this should’ve been df=2
need to redo
X
X
X

## Slide 11: Repeat for the other 194,000 voxels…
Huettel, Song & McCarthy, 2008
First-level analysis
Second-level analysis

## Slide 12: If you really want to be correct…
We often refer to this type of analysis as random effects (RFX)
Since subjects is a random effect but other aspects (e.g., stimulus categories) are fixed effects, technically the proper term is Mixed Effects Analysis
Other common jargon = Second-level Analysis